## Slide 1
VANGUARD-WSN
10.21× Lifetime Extension via Utility-Driven Routing
A Breakthrough in Sustainable IoT Infrastructure
Deepika A · Aishvarya G · Gayatri K · Anjana A
Department of Mathematics · Amrita Vishwa Vidyapeetham
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics

## Slide 2
PROBLEM & OBJECTIVES
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
The Energy Hole Problem
Why existing wireless sensor networks fail prematurely
Energy Hole Phenomenon
Relay nodes near the base station carry all traffic and die first — even if distant nodes have 80% battery remaining.
Legacy Protocol Failure
LEACH picks cluster heads by random dice roll — often selecting exhausted nodes, causing abrupt network collapse.
Our Objective
Replace chance with deterministic logic. Maximize stability (FND) and throughput. Approach the theoretical God-Line LP Bound.

## Slide 3
PROBLEM & OBJECTIVES
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Literature Survey: Comparative Gaps

## Slide 4
SYSTEM ARCHITECTURE
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
System Operation Flow
Every round: sense → rank → route → transmit → repeat
1
INITIALIZATION
BS placement & node random deployment
2
HEARTBEAT
Global health check — all nodes report battery status
3
CONTROL PLANE
Utility index computed at Base Station for all nodes
4
ROUTING
EBPT Tree constructed with energy-balanced paths
5
TRANSMISSION
Data relay cycle executes — plan refreshes next round
Figure 3: Energy-Balanced Path Tree (EBPT)

## Slide 5
PROPOSED MODEL
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Proposed Model: The Vanguard Framework
IMPLEMENTATION
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Rigorous, standards-based implementation
Hybrid Design: SDN Centralized + Tree Routing
Utility Function (Ui): Prioritizes energy over distance.
EBPT Algorithm: Ensures data moves toward sink via healthy nodes.
Acyclic Guarantee: Deterministic DAG logic eliminates loops.
Adaptive Gamma: Dynamically balances load as battery dies.

## Slide 6
PROPOSED MODEL
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Utility-Based Leader Selection
Selecting leaders based on 'Fitness' not 'Luck' — a deterministic, data-driven approach
Utility Index Formula
U(n) = α · E_residual(n) / E_max + (1 − α) / d_avg(n)
Energy Component
Higher residual battery → higher score. We never pick a dying node to lead traffic.
Density Component
Nodes in less-crowded zones score higher. Prevents spatial hotspots from forming.
Elite Set Filter
Only nodes exceeding the network-wide mean utility are even considered as candidates.

## Slide 7
PROPOSED MODEL
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
EBPT Routing + Adaptive Gamma Factor
The two mechanisms that eliminate energy imbalance
Energy-Balanced Path Tree (EBPT)
Multi-hop tree that prioritizes high-energy relay nodes at every step.
Each node selects a parent closer to the sink based on remaining battery.
Heavily burdened nodes become 'expensive' — traffic automatically reroutes to fresher paths.
Acyclic directed graph guarantees zero routing loops.
The Adaptive Gamma Factor (γ)
γ = LOW — Prioritize speed & shorter hops
γ = HIGH — Maximize fairness & absolute longevity
Figure 1: Hierarchical Multi-hop Architecture

## Slide 8
IMPLEMENTATION
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Simulation Environment & Tools
Rigorous, standards-based implementation
Python 3.8+
Core simulation engine — same language powering modern AI.
NumPy + SciPy
Vectorized heuristics & distance matrix geometry.
Matplotlib
Spatial heatmaps, lifetime curves, and comparative charts.
First-Order Radio Model
IEEE standard physics for real-world battery drain.
Table 1: Simulation Parameters

## Slide 9
Implementation: Executed Output Receipt
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
5. Implementation: Executed Output Receipt
5. Implementation: Executed Output Receipt

## Slide 10
RESULTS: NETWORK STABILITY
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Result 1: Network Lifetime — 10.21× Improvement
Figure 5: Network Lifetime Comparison (50 Nodes)
Figure 6: First & Last Node Death Rounds
97
LEACH (Det) FND
993
Vanguard FND
10.21×
Stability Gain
92.1%
of LP Bound (God-Line)

## Slide 11
RESULTS: DATA PRODUCTIVITY
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Result 2: 9.55x More Data Delivered
Because sensors survive longer, they keep transmitting
Figure 8: Cumulative Network Throughput Comparison
118,500
Vanguard-WSN packets
12,400
LEACH (Det) packets
955%
Throughput increase

## Slide 12
RESULTS: ENERGY DISTRIBUTION
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Result 3: Perfect Spatial Energy Balance
Visual proof of the heatmap — no hotspots, no holes
Figure 9: Spatial Energy Consumption — Baseline (left) vs. Vanguard-WSN (right)
Baseline (Left)
Deep red hotspots near center — classic Energy Hole. Nearby nodes exhausted while outer nodes waste full batteries.
Vanguard (Right)
Uniform warm gradient across the field. Every node shares the relay burden proportionally. Zero bottleneck zones.
Fig 7: Energy Fairness Curve

## Slide 13
RESULTS: ENERGY DISTRIBUTION
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Result 3: Perfect Spatial Energy Balance
Visual proof of the heatmap — no hotspots, no holes
Baseline (Left)
Deep red hotspots near center — classic Energy Hole. Nearby nodes exhausted while outer nodes waste full batteries.
Vanguard (Right)
Uniform warm gradient across the field. Every node shares the relay burden proportionally. Zero bottleneck zones.
Fig 7: Energy Fairness Curve

## Slide 14
RESULTS: EXECUTIVE SUMMARY
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Result 4: Comparative Performance Summary
Table 2: Performance Comparison (50 Nodes)
Table 3: Ablation Study
Key Takeaways
10.21×
FND improvement over LEACH (Det)
9.98×
Even LEACH (E-Aware) falls short
92.1%
Of the theoretical LP optimum
0.156
Jain's Fairness Index achieved

## Slide 15
CHALLENGES & FUTURE WORK
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Limitations & What Comes Next
Honest assessment and the road forward
Centralized Overhead
Roll-call chatter uses a small battery 'tax' each round. Accounted for in our model but non-zero.
Timing Idealization
Simulation assumes perfect synchronization. Real radio deployments face interference and timing jitter.
Scalability at Range
A single Brain may be too far from outer nodes in very large deployments spanning multiple kilometers.
Figure 4: Lifetime-Fairness Pareto Frontier
RL-Based Auto-Tuning — Reinforcement learning for dynamic Gamma tuning without human intervention.
Hardware Deployment — Deploy algorithm on real Raspberry Pi / Arduino sensor nodes in the field.

## Slide 16
REFERENCES & ACKNOWLEDGMENTS
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
Sources & Acknowledgments
[1] Heinzelman et al. — 'Energy-Efficient Communication Protocols for Wireless Microsensor Networks.' IEEE HICSS, 2000.
[2] Younis & Fahmy — 'HEED: A Hybrid, Energy-Efficient, Distributed Clustering Approach.' IEEE Trans. Mobile Computing, 2004.
[3] Lindsey et al. — 'PEGASIS: Power-Efficient Gathering in Sensor Information Systems.' IEEE Aerospace, 2002.
[4] Vanguard Implementation — 'Utility-Driven EBPT Framework.' Department of Mathematics, Amrita Vishwa Vidyapeetham, 2026.
[5] First-Order Radio Model — IEEE Standard for Low-Power Wireless Sensor Physics.
Department of Mathematics · Amrita Vishwa Vidyapeetham
All figures generated using Python · Matplotlib · NetworkX

## Slide 17
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics
In Summary
Vanguard-WSN Delivers
10.21×
Longer network lifetime (FND)
92.1%
Approach to the LP theoretical optimum
955%
More cumulative data delivered
0 holes
Zero energy hotspots — perfectly balanced
"Reliable data starts with a reliable network."
Thank You
Questions & Discussion
VANGUARD-WSN · Amrita Vishwa Vidyapeetham · Dept. of Mathematics